## Slide 1: Preliminary Design Review
Team 10
Carlos Jones, Aiden Deady, Manas Pise
RBE 3002 D24

## Slide 2: Functionality (Overall)
Phase 1:
Navigate through unknown maze, mapping the space
Use heuristic costs between frontier points
Stop navigating after entirety of map is discovered
Phase 2:
Navigate back to starting point from the current location
Phase 3:
Use AMCL to self-localize location on map from Phase 1.
Navigate to given set of coordinates after localizing

## Slide 3: Functionality (Phase 1)
GMapping:
Detect the walls and obstacles as OccupancyGrid
Pass the generate map in order to calculate C Space
Identifying Frontiers:
Centroid of open space at edge of known space
Heuristic
  Distance from current location to frontier
  Chooses lowest cost that is first in queue
If robot is stuck:
  Returns to most recent known location
  Spins until unstuck

## Slide 4: Functionality (Phase 2)
Path Planning:
Buffer C Space to avoid walls
Path does not have to be optimal, just mostly efficient
Given starting location and goal location:
  Move through map to reach goal

## Slide 5: Functionality (Phase 3)
AMCL:
Uses map from Phase 1
Laser scans to localize robot location relevant to map
Identifying Location:
Robot does 360 at start to understand starting location and orientation
If robot is still not localized:
  Follow a wall or drive to unobstructed point
    Able to gather more data of area surrounding location

## Slide 6: Architecture

## Slide 7: Risks and Challenges
Potential slippage or error:
Slower robot speed results in less potential for error
C Space buffer will provide more room for potential error
Re-localization once robot reaches a frontier should reset error build up
LIDAR interference or inconsistency:
There is more room for error with slight inaccuracies in readings. Overall path and movement can still be efficient.
This should not be a major issue.